## Slide 1: Analysing Railway Infrastructure utilisation
A Geospatial Approach
Stuart Gordon
Supervisors: Dr Craig Robson, Professor Roberto Palacin
Oliver Bratton (Network Rail)

## Slide 2
Capacity
  Infrastructure
  Systems
  Train Service
Utilisation
  Efficiency
  Performance vs Capacity
Uses
  Investment
  Planning
  Performance Monitoring
Abril et al, 2008. An assessment of railway capacity. Transportation Research Part E: Logistics and Transportation Review, 44(5), pp.774-806.
Railway Capacity & Utilisation
Notes: Railway Capacity
Definition: Maximum number of trains that can safely run on a railway line in a given period.
Factors Determining Capacity:
  Track infrastructure (single/double/multiple tracks).
  Signaling systems.
  Frequency of train services.
  Track maintenance schedules.
Capacity Enhancement:
  Track upgrades (adding additional tracks).
  Improved signaling technology.
  Reduction of bottlenecks (e.g., junctions).
  Station improvements (e.g., platform extensions).
Railway Utilisation
Definition: Actual number of trains running on a railway line compared to its capacity.
Significance:
  Reflects efficiency of the railway system.
  Indicator of congestion and potential delays.
Optimal Utilisation: Ensures a balance between high service levels and the ability to accommodate unexpected disruptions.
Over-Utilisation Risks:
  Increased delays.
  Reduced safety margins.
  Faster wear and tear of infrastructure.
Why & How It's Used
Planning & Investment:
Timetable Creation:
Pricing Decisions:
Performance Metrics:
Safety:
Customer Satisfaction:

## Slide 3: Railway Capacity & Utilisation
Capacity
  Infrastructure
  Systems
  Train Service
Utilisation
  Efficiency
  Performance vs Capacity
Uses
  Investment
  Planning
  Performance Monitoring
Landex, A. Evaluation of Railway Networks with Single Track Operation Using the UIC 406 Capacity Method. Netw Spat Econ 9, 7–23 (2009). https://doi.org/10.1007/s11067-008-9090-7
Notes: Railway Capacity
Definition: Maximum number of trains that can safely run on a railway line in a given period.
Factors Determining Capacity:
  Track infrastructure (single/double/multiple tracks).
  Signaling systems.
  Frequency of train services.
  Track maintenance schedules.
Capacity Enhancement:
  Track upgrades (adding additional tracks).
  Improved signaling technology.
  Reduction of bottlenecks (e.g., junctions).
  Station improvements (e.g., platform extensions).
Railway Utilisation
Definition: Actual number of trains running on a railway line compared to its capacity.
Significance:
  Reflects efficiency of the railway system.
  Indicator of congestion and potential delays.
Optimal Utilisation: Ensures a balance between high service levels and the ability to accommodate unexpected disruptions.
Over-Utilisation Risks:
  Increased delays.
  Reduced safety margins.
  Faster wear and tear of infrastructure.
Why & How It's Used
Planning & Investment:
Timetable Creation:
Pricing Decisions:
Performance Metrics:
Safety:
Customer Satisfaction:
Literature
Logical Infrastructure linked to Timetable
Standard Approach UIC406
Simulation over topological models
Rare use of empirical data
No validation of real world predictions
Many variations of methods and ways to optimize

## Slide 4: Existing Methods
Timetable Compression
Analytical Methods
Optimization
Modeling & Simulation based
Topological Network Models
Landex, A. Evaluation of Railway Networks with Single Track Operation Using the UIC 406 Capacity Method. Netw Spat Econ 9, 7–23 (2009). https://doi.org/10.1007/s11067-008-9090-7
Notes: Landex, A. Evaluation of Railway Networks with Single Track Operation Using the UIC 406 Capacity Method. Netw Spat Econ 9, 7–23 (2009). https://doi.org/10.1007/s11067-008-9090-7

## Slide 5
Aims
Investigate Utilisation
Compare Planned against Actual Utilisation
Identify Events or Incidents

## Slide 6
Objectives
Geospatial Infrastructure
Spatial Temporal Graphs
Identify Differences in Utilisation
Realtime Processing

## Slide 7
Data Preparation
Data Processing
Calculation
Methodology

## Slide 8
Data Preparation
Data Processing
Calculation
Process

## Slide 9
Over 20,000 Miles
15,416 edges
Scope

## Slide 10
Geospatial Model
Physical Assets
Data Preparation

## Slide 11
Logical Diagram
Logical Path
Data Processing

## Slide 12
Actual Network Path
Predict Planned Path
  Probabilistic Prediction Model
  Modal next edge
  Mean edge duration
Data Processing
A1 A2 Train Describer Networks
An Actual Network Path
Pln Timetabled locations
Prn Predicted Planned Path
Tn Transitions between Networks

## Slide 13
Geospatial Route
Utilisation
Calculation

## Slide 14
Geospatial Route
Utilisation
Calculation

## Slide 15
Data quality
Data availability
Impact of Poor Data
Challenges

## Slide 16
Data quality
Data availability
Impact of Poor Data
Challenges

## Slide 17
11th to 23rd July 2023
26.5 million train movements
7.8 million planned locations
149,473 out of 181,181 trains successfully calculated (82.50%)
Results
Normalized Actual Utilisation
Normalized Planned Utilisation

## Slide 18
Industrial Action 20th July
On Strike:
  TransPennine Express
  Northern
  Avanti West Coast
Not On strike:
  Merseyrail
  Transport for Wales
Results
19th July Normalized Actual Utilisation
20th July Normalized Actual Utilisation

## Slide 19
Industrial Action 20th July
On Strike:
  TransPennine Express
  Northern
  Avanti West Coast
Not On strike:
  Merseyrail
  Transport for Wales
Results
Actual Difference between 19th & 20th July 2023

## Slide 20
Method has potential, strike days indicate this
Currently limited by data quality and availability
Conclusions
Actual Difference between 19th & 20th July 2023

## Slide 21
Data Quality Improvements
Utilisation & Capacity Methods
Realtime
Incident Detection
  Historical Analysis
  Realtime Detection
Further Work

## Slide 22
Data Quality Improvements
Utilisation & Capacity Methods
Realtime
Incident Detection
  Historical Analysis
  Realtime Detection
Further Work

## Slide 23: Analysing Railway Infrastructure utilisation A Geospatial Approach
Any Questions?
Further details